## Slide 1
A team can have up to 4 members including the team leader. Add rows if necessary.
Team Details
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
Team Solverz
Ankan Mondal
4th Year
Shivam Garg
4th Year
Saksham Tikariha
4th Year
National Institute of Technology Raipur
+91-9668130904
ankanmondalclass1@gmail.com
Notes: 2

## Slide 2
Problem Statement Addressed
Drift-Sense: AI-Powered Navigation-Error Recovery for Wafer Inspection Tools
Why Navigation Errors Matter
  Wafer inspection tools must repeatedly revisit the same relative location across thousands of repeated die patterns
  Stage drift, vibration, and thermal effects cause the tool to land off-target
  Result: mis-navigated inspection → unreliable defect/metrology data
The Challenge
  Given a 100x reference image (exact prior target, high-res) and a 10x search image (wider current view, lower-res)
  Locate the reference pattern inside the search image at ~10:1 scale
  Return precise target-centre coordinates (x, y)
  Resolve repeated-pattern ambiguity → pick match closest to search-image centre
The Task
  Throughput: Every mis-navigation event slows expensive, shared fab tools
  Yield accuracy: Wrong location = unreliable defect detection → false alarms or missed defects
  Pattern ambiguity is the hard part: Repetitive dies make naive matching lock onto the wrong (but identical-looking) site
  Real-world robustness: Must survive noise, blur, scale (9:1–11:1) & rotation (1–2°) — not just clean synthetic pairs
Why It's Significant
Notes: 3

## Slide 3
Idea Description
KEY CONCEPT & APPROACH
  Recover the drifted navigation location via multi-scale Normalized Cross-Correlation (NCC) template matching
  Treat the 10:1 magnification as unknown-but-bounded — search scales 9x–11x rather than assuming an exact ratio
  Score every candidate location across all scales; retain all strong matches, not just the single best
  Resolve repeated-pattern ambiguity by selecting the match closest to the search-image centre
SOLUTION OVERVIEW
  Pre-processing: Trim artificial crop-boundary pixels from the reference so edge brightening doesn't bias matching
  Multi-scale search: Downsample the reference at each candidate scale (step 0.2x) and run cv2.matchTemplate against the search image
  Candidate extraction: Use local-maxima filtering at each scale to surface every plausible location
  Match selection: Keep candidates within a score window (best − 5%) of the top NCC score
  Disambiguation rule: Among remaining valid matches, output the one whose centre is nearest the search-image centre
  Output: Predicted (x, y) target centre in search-image pixels, annotated visualization of all candidates, NCC confidence score, and measured runtime
Notes: 4

## Slide 4
Proposed Solution
SOLUTION DETAILS
  Multi-scale Normalized Cross-Correlation (NCC) template matching to recover drifted navigation locations
  Reference image pre-processed by trimming crop-boundary pixels to remove artificial edge bias
  Reference resampled across a scale sweep (9x–11x, step 0.2x) to explicitly account for magnification uncertainty rather than assuming an exact 10:1 ratio
  Template matched against the search image at each scale using OpenCV's TM_CCOEFF_NORMED
  Local-maxima extraction (not global max alone) surfaces every plausible candidate per scale
Methodology
Technologies Involved
  Python, OpenCV (cv2.matchTemplate, cv2.resize)
  NumPy for array operations and scoring
  SciPy (maximum_filter) for local peak/candidate detection
Match Selection & Disambiguation
  Candidates within a score window (best NCC − 5%) are retained as valid matches
  Spatially duplicate detections across nearby scales are collapsed to one per true location
  Final prediction = valid match whose centre is closest to the search-image centre (handles repeated-pattern ambiguity)
Implementation Strategy
  Output: predicted (x, y) target centre, NCC confidence score, annotated visualization, and measured runtime
  Explicit scale-aware matching directly satisfies the 10:1 magnification requirement
  Runs repeatably on batches of reference/search pairs without manual code changes
Realistic Defects Simulated
  Blur — spot-size/astigmatism-like defocus
  Angle tilt (±0.05–2°) — stage/wafer misalignment
  Repetition increase — duplicated/mirrored patches modelling die-pattern ambiguity
  Edge stress — charging/edge brightness gradients
  Scale mismatch (9x–11x) — real magnification drift
  Black/white tint — contrast/gamma drift
  Scanline noise & line dropouts — raster-scan acquisition artifacts
  Brightness drift — thermal/detector drift over a scan
  Each defect is physically motivated, randomized per sample, and can be composed with others; seed and parameters logged per pair for reproducibility
Realistic Defects Simulated
  Solves cross-magnification localization under scale (9:1–11:1) and rotation (1–2°) variation
  Robust to SEM-style degradation via score-window tolerance and defect-hardened training data
  Resolves repeated die-pattern ambiguity using the centre-proximity tie-break rule
Notes: 5

## Slide 5
Innovation and Uniqueness
KEY INNOVATION
COMPETITIVE ADVANTAGE
  Physics-inspired synthetic DRAM environment: Generates continuous, hierarchical DRAM layouts with correlated pitches, multiple bank topologies, routing intersections and repeated structures rather than simple tiled patterns.
  Explicit 10:1 scale reasoning: The 100× reference is systematically converted to the expected 10× search-image scale, while evaluating 9×–11× candidates to tolerate magnification uncertainty.
  Multi-candidate localization: Instead of blindly accepting the single highest correlation, the system retains spatially distinct high-confidence candidates and resolves repeated-pattern ambiguity using the problem's centre-selection rule.
  Reproducible degradation framework: Noise, blur, scale mismatch, brightness drift, scanline artifacts, line dropouts and other degradations can be systematically introduced while retaining ground-truth metadata.
Scale-Aware DRAM Navigation Recovery with Ambiguity-Aware Matching
Accuracy-focused without unnecessary model complexity
  No training dependency: Uses classical computer vision with normalized cross-correlation, making the localization pipeline deterministic and avoiding dependence on pretrained neural-network weights.
  Robust to scale uncertainty: Searches across 9×–11× rather than assuming an exact 10× relationship, directly addressing a stated evaluation condition.
  Designed for repetitive semiconductor structures: Spatially distinct candidates are preserved rather than incorrectly suppressing physically different repeated patterns.
  Evaluator-ready output: Produces predicted centre coordinates, matching scale, NCC score, candidate locations and a visualized localization result.
  Computationally practical architecture: The inference path is based on OpenCV/NumPy/SciPy operations rather than a large learned model, providing a strong basis for CPU/edge deployment—subject to measured runtime and hardware validation.
Notes: 6

## Slide 6
Impact and Benefits
Primary Impact
  Reduces manual re-localization
  Improves inspection continuity
  Handles repetitive wafer patterns
  Robust to magnification uncertainty
  Low deployment complexity
  Low computational cost
  no extensive training dataset required
Quantifiable Outcomes
  11 Scale hypotheses
9×–11× @ 0.2×
  ≤5 Distinct candidate locations
before final selection
  0.05 NCC
Acceptance window
relative to best match
  ≥30 Independent test pairs
validation requirement
  400 ms Average inference time
per image pair
Automated Recovery of Wafer-Inspection Navigation Errors
Notes: 7

## Slide 7
Technology & Feasibility/Methodology Used
IMPLEMENTATION STRATEGY
Procedural DRAM → SEM Degradation → Scale-Aware Matching → Ambiguity Resolution → Quantitative Validation
Software Architecture
Hardware Components
Development Tools
  Generate: 1000×1000 grayscale DRAM reference/search pairs with exact ground truth.
  Degrade: Apply controlled blur, noise, drift, scanline and feature-loss effects.
  Localize: Search 9×–11× scales using NCC template matching.
  Resolve: Retain spatially distinct candidates and select the valid match closest to image centre.
  Validate: Report localization error, threshold-wise accuracy and runtime.
Python • OpenCV • NumPy • SciPy • Pillow
• CPU • RAM
• No dedicated GPU required
Python • Git/GitHub • CSV/JSON
• README/requirements
Notes: 8

## Slide 8
GitHub & Video Link
GitHub Repository
github
Prototype / Simulation Video
Video
Notes: 9

## Slide 9
Research and References
Research Background & Methodology
  DRAM structure:
Repeated word-line/bit-line arrays + hierarchical bank organization → realistic synthetic DRAM topology
  SEM degradation:
Blur + noise + drift + charging/scan artifacts + feature loss → controlled robustness testing
  Localization:
Multi-scale normalized correlation + candidate analysis → scale-aware navigation recovery
  Validation:
Ground-truth coordinates + Euclidean error + threshold pass rates → quantitative evaluation
References & Citations
List key papers, articles, or data sources.
https://irds.ieee.org/images/files/pdf/2017/2017IRDS_MM.pdf
https://irds.ieee.org/images/files/pdf/2024/2024IRDS_MM.pdf
https://semiengineering.com/7nm-fab-challenges/
https://docs.opencv.org/4.13.0/d4/dc6/tutorial_py_template_matching.html
Notes: 10